## Slide 1: Chapter 12
Path Planning

## Slide 2: Control Architecture
path planner
path manager
path following
autopilot
unmanned aircraft
waypoints
on-board sensors
position error
tracking error
status
destination, obstacles
servo commands
state estimator
wind
path definition
airspeed, altitude,
heading,
commands
map

## Slide 3: Path Planning Approaches
Deliberative
  Based on global world knowledge
  Requires a good map of terrain, obstacles, etc.
  Can be too computationally intense for dynamic environments
  Usually executed before the mission
Reactive
  Based on what sensors detect on immediate horizon
  Can respond to dynamic environments
  Not usually used for entire mission

## Slide 4: Voronoi Graphs
Notes: \begin{itemize}
\item For finite number $\mathcal{Q}$ point obstacles, Voronoi graph \\ divides search plane into $\mathcal{Q}$ convex cells, each containing \\ one point obstacle
\item Interior of cell is closer to its point than any other point in $\mathcal{Q}$
\item Edges of graph are perpendicular bisectors between points in $\mathcal{Q}$
\item Edges of path maximize distance from point obstacles
\end{itemize}

## Slide 5: Voronoi Graph Example
Graph generated using voronoi command in Matlab
20 point obstacles
Start and end points of path not shown

## Slide 6: Voronoi Graph Example
Add start and end points to graph
Find 3 closest graph nodes to start and end points
Add graph edges to start and end points
Search graph to find “best” path
Must define “best”
  Shortest?
  Furthest from obstacles?

## Slide 7: Path Cost Calculation
Notes: \noindent
Nodes of graph edge: $\mathbf{v}_1$ and $\mathbf{v}_2$ \\
Point obstacle: $\mathbf{p}$
\vspace{0.5cm}
\noindent Length of edge: $\norm{\mathbf{v}_1-\mathbf{v}_2}$
\vspace{0.5cm}
\noindent Any point on line segment:
$\mathbf{w}(\sigma) = (1-\sigma)\mathbf{v}_1 + \sigma \mathbf{v}_2$ where $\sigma\in[0,1]$
\vspace{0.5cm}
\noindent
Minimum distance between
$\mathbf{p}$ and graph edge
\begin{align*}
D(\mathbf{v}_1,\mathbf{v}_2,\mathbf{p}) &\defeq
\min_{\sigma\in[0,1]}\norm{\mathbf{p}-\mathbf{w}(\sigma)} \\
&=\min_{\sigma\in[0,1]} \sqrt{ (\mathbf{p}-\mathbf{w}(\sigma))^{\top}(\mathbf{p}-\mathbf{w}(\sigma)) } \\
&=\min_{\sigma\in[0,1]} \sqrt{
\norm{\mathbf{p}-\mathbf{v}_1}^2
+ 2\sigma(\mathbf{p}-\mathbf{v}_1)^{\top}(\mathbf{v}_1-\mathbf{v}_2) +
\sigma^2\norm{\mathbf{v}_1-\mathbf{v}_2}^2}.
\end{align*}

## Slide 8: Path Cost Calculation
Notes: \noindent Value for $\sigma$ that minimizes $D$ is
\[
\sigma^{\ast} = \frac{(\mathbf{v}_1-\mathbf{p})^{\top}
(\mathbf{v}_1-\mathbf{v}_2)}{\norm{\mathbf{v}_1-\mathbf{v}_2}^2}
\]
\noindent Location along edge for which $D$ is minimum:
\[
\mathbf{w}(\sigma^{\ast}) = \sqrt{\norm{\mathbf{p}-\mathbf{v}_1}^2 -
\frac{\left((\mathbf{v}_1-\mathbf{p})^{\top}(\mathbf{v}_1-\mathbf{v}_2)\right)^2}{\norm{\mathbf{v}_1-\mathbf{v}_2}^2}}
\]
\noindent Define distance to edge for $\sigma^\ast<0$, $\sigma^\ast>1$:
\[
D^{'}(\mathbf{v}_1,\mathbf{v}_2,\mathbf{p}) \defeq
\begin{cases} %
\mathbf{w}(\sigma^{\ast}) & \text{~if~} \sigma^{\ast}\in[0,1] \\
\norm{\mathbf{p}-\mathbf{v}_1} & \text{~if~} \sigma^{\ast}<0 \\
\norm{\mathbf{p}-\mathbf{v}_2} & \text{~if~} \sigma^{\ast}>1
\end{cases}
\]
\noindent Distance between point set $\mathcal{Q}$ and line segment $\overline{\mathbf{v}_1\mathbf{v}_2}$:
\[
D(\mathbf{v}_1,\mathbf{v}_2,\mathcal{Q}) = \min_{\mathbf{p}\in\mathcal{Q}} D^{'}(\mathbf{v}_1,\mathbf{v}_2,\mathbf{p})
\]

## Slide 9: Path Cost Calculation
Notes: \noindent Cost for traveling along edge $(\mathbf{v}_1,\mathbf{v}_2)$ is assigned as
\begin{equation*}
J(\mathbf{v}_1,\mathbf{v}_2) = \underbrace{k_1 \norm{\mathbf{v}_1-\mathbf{v}_2}}_\text{length of edge} +
\underbrace{\frac{k_2}{D(\mathbf{v}_1,\mathbf{v}_2,\mathcal{Q})}}_\text{reciprocal of distance to closest point in $\mathcal{Q}$}
\end{equation*}
\vspace{0.5cm}
\noindent $k_1$ and $k_2$ are positive weights
\vspace{0.5cm}
\noindent Choice of $k_1$ and $k_2$ allow tradeoff between path length and proximity to threats.

## Slide 10: Voronoi Path Planning Algorithm
Dijkstra’s algorithm is used to search the graph
Voronoi graph and Dijkstra’s algorithm code are commonly available
Matlab:
Voronoi -> voronoi
Dijkstra -> shortestpath

## Slide 11: Voronoi Path Planning Result

## Slide 12: Voronoi Path Planning – Non-point Obstacles
How do we handle solid obstacles?
Point obstacles at center of spatial obstacles won’t provide safe path options around obstacles

## Slide 13: Non-point Obstacles – Step 1
Insert points around perimeter of obstacles

## Slide 14: Non-point Obstacles – Step 2
Construct Voronoi graph
Note infeasible path edges inside obstacles

## Slide 15: Non-point Obstacles – Step 3
Remove infeasible path edges from graph
Search graph for best path

## Slide 16: Rapidly Exploring Random Trees (RRT)
Exploration algorithm that randomly, but uniformly explores search space
Can accommodate vehicles with complicated, nonlinear dynamics
Obstacles represented in a terrain map
Map can be queried to detect possible collisions
RRTs can be used to generate a single feasible path or a tree with many feasible paths that can be searched to determine the best one
If algorithm runs long enough, the optimal path through the terrain will be found

## Slide 17: RRT Tree Structure
RRT algorithm is implemented using tree data structure
Tree is special case of directed graph
Edges are directed from child node to parent
Every node has one parent, except root
Nodes represent physical states or configurations
Edges represent feasible paths between states
Each edge has cost associated traversing feasible path between states

## Slide 18: RRT Algorithm
Algorithm initialized
  start node
  end node
  terrain/obstacle map

## Slide 19: RRT Algorithm
Notes: \begin{itemize}
\item Randomly select configuration $\mathbf{p}$ in workspace
\item Select new configuration $\mathbf{v}_1$ fixed distance $D$ from start point along line connecting $\mathbf{p}_s$ and $\mathbf{p}$
\item Check new segment for collisions
\item If collision-free, insert $\mathbf{v}_1$ into tree.
\end{itemize}

## Slide 20
RRT Algorithm
Notes: \begin{itemize}
\item Generate random configuration $\mathbf{p}$ in workspace
\item Search tree to find node closest to $\mathbf{p}$
\item From node closest to $\mathbf{p}$, move distance $D$ along line connecting node and $\mathbf{p}$ to establish configuration $\mathbf{v}_2$
\item Check new segment for collisions
\item If collision-free, insert $\mathbf{v}_2$ into tree
\end{itemize}

## Slide 21
RRT Algorithm
Notes: \begin{itemize}
\item Generate random configuration $\mathbf{p}$ in workspace
\item Search tree to find node closest to $\mathbf{p}$
\item From node closest to $\mathbf{p}$, move distance $D$ along line connecting node and $\mathbf{p}$ to establish new node
\item Check new segment for collisions
\item If collision-free, insert new node into tree
\end{itemize}

## Slide 22
RRT Algorithm
Continue adding nodes and checking for collisions

## Slide 23
RRT Algorithm
Continue until node is generated that is within distance D of end node
At this point, terminate algorithm or search for additional feasible paths

## Slide 24: RRT Algorithm

## Slide 25: Path Smoothing
Start with initial point (1)
Make connections to subsequent points in path (2), (3), (4) …
When connection collides with obstacle, add previous waypoint to smoothed path
Continue smoothing from this point to end of path

## Slide 26: Path Smoothing Algorithm

## Slide 27: RRT Results

## Slide 28
RRT Results

## Slide 29
RRT Results

## Slide 30
RRT Results

## Slide 31
RRT* Algorithm – Extend Step
Notes: \begin{itemize}
\item Generate new potential node $\mathbf{v}_{new}$ identical to RRT.
\item Instead of finding the closest node in the tree, find all nodes within neighborhood $\mathcal{N}$.
\item Let $C(\mathbf{v})$ be the path cost from $\mathbf{p}_s$ to $\mathbf{v}$, and let $c(\mathbf{v}_1,\mathbf{v}_2)$ be the path cost from $\mathbf{v}_1$ to $\mathbf{v}_2$.
\item Let $\mathbf{v}' = \arg\min_{\mathbf{v}\in \mathcal{N}}\left(C(\mathbf{v}) + c(\mathbf{v}_{new}, \mathbf{v})\right)$ (i.e., closest node in $\mathcal{N}$ to $\mathbf{v}_{new}$).
\item Add node $V\leftarrow V \bigcup \{\mathbf{v}_{new}\}$.
\item Add edge $E\leftarrow E\bigcup\{(\mathbf{v}',\mathbf{v}_{new})\}$.
\item Set $C(\mathbf{v}_{new}) = C(\mathbf{v}') + c(\mathbf{v}_{new}, \mathbf{v})$.
\end{itemize}

## Slide 32
RRT* Algorithm – Re-wire Step
Notes: \begin{itemize}
\item Generate new potential node $\mathbf{v}_{new}$ identical to RRT.
\item Instead of finding the closest node in the tree, find all nodes within neighborhood $\mathcal{N}$.
\item Let $C(\mathbf{v})$ be the path cost from $\mathbf{p}_s$ to $\mathbf{v}$, and let $c(\mathbf{v}_1,\mathbf{v}_2)$ be the path cost from $\mathbf{v}_1$ to $\mathbf{v}_2$.
\item Let $\mathbf{v}' = \arg\min_{\mathbf{v}\in \mathcal{N}}\left(C(\mathbf{v}) + c(\mathbf{v}_{new}, \mathbf{v})\right)$ (i.e., closest node in $\mathcal{N}$ to $\mathbf{v}_{new}$).
\item Add node $V\leftarrow V \bigcup \{\mathbf{v}_{new}\}$.
\item Add edge $E\leftarrow E\bigcup\{(\mathbf{v}',\mathbf{v}_{new})\}$.
\item Set $C(\mathbf{v}_{new}) = C(\mathbf{v}') + c(\mathbf{v}_{new}, \mathbf{v})$.
\end{itemize}

## Slide 33
RRT vs. RRT*
From S. Karaman and E. Frazzoli, “Incremental Sampling-based Algorithms for
Optimal Motion Planning,” International Journal of Robotic Research, 2010.

## Slide 34
RRT vs. RRT*
From S. Karaman and E. Frazzoli, “Incremental Sampling-based Algorithms for
Optimal Motion Planning,” International Journal of Robotic Research, 2010.

## Slide 35: RRT Path Planning Over 3D Terrain
Assume terrain map can be queried to determine altitude of terrain at any north-east location
Must be able to determine altitude for random configuration p in RRT algorithm
Must be able to detect collisions with terrain – reject random candidate paths leading to collision
Options:
  random altitude within predetermined range
  random selection of discrete altitudes in desired range
  set altitude above ground level
Test candidate paths to ensure flight path angles are feasible – reject if infeasible

## Slide 36: RRT Algorithm – 3D Terrain
modify to test for collisions
with terrain and flight path
angle feasibility

## Slide 37: RRT 3D Terrain Results

## Slide 38: RRT 3D Terrain Results

## Slide 39: RRT 3D Terrain Results

## Slide 40: RRT Dubins Approach
To generate a new random configuration for tree:
  Generate random N-E position in environment
  Find closest node in RRT graph to new random point
  Select a position of distance L from the closest RRT node in direction of new point – use this position as N-E coordinates of new configuration
  Define course angle for new configuration as the angle of the line connecting the RRT graph to the new configuration

## Slide 41: RRT Algorithm - Dubins
Notes: \begin{itemize}
\item Randomly select configuration $\mathbf{p}$ in workspace
\item Select new configuration $\mathbf{v}_1$ fixed distance $D$ from start point along line connecting $\mathbf{p}_s$ and $\mathbf{p}$
\item Check new segment for collisions
\item If collision-free, insert $\mathbf{v}_1$ into tree.
\end{itemize}

## Slide 42: RRT Algorithm - Dubins
Notes: \begin{itemize}
\item Randomly select configuration $\mathbf{p}$ in workspace
\item Select new configuration $\mathbf{v}_1$ fixed distance $D$ from start point along line connecting $\mathbf{p}_s$ and $\mathbf{p}$
\item Check new segment for collisions
\item If collision-free, insert $\mathbf{v}_1$ into tree.
\end{itemize}

## Slide 43: RRT Algorithm - Dubins
Collision
Notes: \begin{itemize}
\item Randomly select configuration $\mathbf{p}$ in workspace
\item Select new configuration $\mathbf{v}_1$ fixed distance $D$ from start point along line connecting $\mathbf{p}_s$ and $\mathbf{p}$
\item Check new segment for collisions
\item If collision-free, insert $\mathbf{v}_1$ into tree.
\end{itemize}

## Slide 44: RRT Algorithm - Dubins
Continue adding nodes and checking for collisions
Notes: \begin{itemize}
\item Randomly select configuration $\mathbf{p}$ in workspace
\item Select new configuration $\mathbf{v}_1$ fixed distance $D$ from start point along line connecting $\mathbf{p}_s$ and $\mathbf{p}$
\item Check new segment for collisions
\item If collision-free, insert $\mathbf{v}_1$ into tree.
\end{itemize}

## Slide 45
RRT Algorithm
Continue until node is generated that is within distance D of end node
At this point, terminate algorithm or search for additional feasible paths

## Slide 46: RRT Dubins Results

## Slide 47: RRT Dubins Results

## Slide 48: RRT Dubins Results

## Slide 49: Coverage Algorithms
Goal: Survey an area
  Pass sensor footprint over entire area
Algorithms often cell based
  Goal: visit every cell

## Slide 50: Coverage Algorithm
Two maps in memory
  terrain map
    used to detect collisions with environment
  coverage or return map
    used to track coverage of terrain
Return map stores value of returning to particular location
  Return map initialized so that all locations have same return value
  As locations are visited, return value of that location is decremented by fixed amount:

## Slide 51: Coverage Algorithm
Finite look ahead tree search used to determine where to go
Tree generated from current MAV configuration
Tree searched to determine path that maximizes return value
Two methods for look ahead tree
  Uniform branching
    Predetermined depth
    Uniform branch length
    Uniform branch separation
  RRT

## Slide 52: Coverage Algorithm

## Slide 53: Coverage Planning Results – Uniform Tree
Look ahead length = 5
Heading change = 30 deg
Tree depth = 3
Iterations = 200

## Slide 54: Coverage Planning Results – Uniform Tree
Look ahead length = 5
Heading change = 60 deg
Tree depth = 3
Iterations = 200

## Slide 55: Coverage Planning Results – RRT Dubins

## Slide 56: Coverage Planning Results – RRT Dubins